## Slide 1: Dynamic Gaze-Contingent Rendering Complexity Scaling
By Luke Paireepinart

## Slide 2: Initial Objectives
Use the eye sensitivity function
Dynamically adjust rendering complexity
Increase average frame rate
Make the degradation as unnoticeable as possible
Complete a real implementation in a single semester
Get extra credit points

## Slide 3: Project Implementation Environment

## Slide 4: Panda3D justification
Made by Disney and CMU
Originally commercial, now Open-Source
Windows support
Commercial Applications & Games
Integrated w/ Python (vs. pyOGRE etc.)
Extremely fast engine
But most of all…..

## Slide 5: Shader Support with
CG vs. HLSL vs. GLSL
Shaders are really neat

## Slide 6: Shader Pipeline
Vertex Shader
  Modifies vertex positions, as well as colors / texcoords (which are LERP’ed)
Geometry Shader
  Creates new vertexes
Pixel / Fragment Shader
  Determines final rendering color of every pixel

## Slide 7: What the heck is LERP?!
Linear IntERPolation

## Slide 8: Shader Complexity
Vertex Shader Speed
  Determined by the number of visible (basically) vertexes in the scene
Fragment Shader Speed
  Run for every pixel on the screen (for specific models w/ fragment shaders applied)

## Slide 9: Example Vertex Shaders

## Slide 10: Example Vertex Shaders

## Slide 11: Example Geometry Shaders

## Slide 12: Example Geometry Shaders

## Slide 13: Example Pixel Shaders

## Slide 14: Example Pixel Shaders

## Slide 15: How ridiculously fast the GPU is
  1680x1050 display = 1,764,000 pixels on screen,
  1920x1200 display = 2,304,000 pixels on screen!
Can have multiple fragment shaders per pixel
8800GT runs my shader at ~700 FPS at 1680x1050
That’s 1,234,800,000 function calls a second!
The 9800GT = $85 new on Newegg
    9800GT == 8800GT (they are EXACTLY the same card)

## Slide 16: Bump Mapping
+ =

## Slide 17: No Live Demonstration
Laptop doesn’t support shaders
Panda3D can’t be installed on school computers
Desktop is enormous & I don’t want to carry it
Screenshots/video will have to do
  I’ll send you the program later if you’re interested and you ask nicely

## Slide 18: Actual Running Example

## Slide 19: Actual Running Example

## Slide 20: Actual Running Example
Youtube Video
It’s much smoother in real life
(recorded at 60 FPS, encoded at 29.97 FPS, result… judder)

## Slide 21: Approach Justification
Bump-mapping is a simple example, but…
  Shader is reusable
  Modifications are easy
  Template could be created
  Could be integrated into every pixel shader automatically by engine
  Could be integrated into vertex / geometry shaders as well

## Slide 22: Deviation from Spec
Render stops at a specific point (no sensitivity function, just a hard drop-off)
vs
No speed gain in areas where rendering is done partially (for most effects)

## Slide 23: Idealistic Goals
Great speedup
Unnoticeable degradation of effect
Easy implementation
  Everyone’s happy!

## Slide 24: Unfortunate Reality
Branching in GPU code is not implemented well
If your code follows two different branches it is not optimized correctly by the compiler, and automatically gets slowed down by about 8%
Even with identical code in both branches, there was still that 8% slowdown if the branch was taken only during certain calls
This may be due to a cache miss, but seems unlikely

## Slide 25: Unfortunate Reality
Bumpmapping creates contrast
Lack of contrast in peripheral is still noticeable
  It’s not necessarily distracting but the effect is not as seamless as you might wish
Updating mouse position creates massive slowdown while mouse is moving
  Still was >400FPS in the example with mouse waving
Notes: Using less aggressive darkening on the bump mapping will likely alleviate both of the bumpmapping issues

## Slide 26: Unfortunate Reality
CG REALLY SUCKS
  Variable passing is not implemented in a sensible manner
  Certain variables have to be copied to a new variable and re-aliased before they’re passed
  Even just ACCESSING the wrong variable can cause everything to break
  NO REALLY, check it out…

## Slide 27: CG Sucks Passthrough Fragment Shader
Commented variable access
//l_position;
o_color = tex2D(tex_0, l_texcoord0);
o_color.w = 1.0;
Uncommented variable access
l_position;
o_color = tex2D(tex_0, l_texcoord0);
o_color.w = 1.0;

## Slide 28: Actual Performance Characteristics
During regular run at 1680x1050 (windowed)
    700-730 FPS with full-screen bumpmapping
    650-700 FPS with area bumpmapping
  During regular run at 1680x1050 (fullscreen)
    Exactly the same as above results
    Yeah, I thought fullscreen would be faster too
  I ran it on Windows XP. On Win7, windowed mode is automatically VSYNCed so FPS would be 60 (for my monitors (and probably yours too))

## Slide 29: How we could make this actually speed up rendering process
GPU branching needs to be made more efficient
Use effects that are so complicated to calculate that the speed improvement is worth the branching slowdown
Modify specific effects to be scaled without a branch (using the distance from center directly)
  But this solution is not as universal as the original and relies on the implementer too much

## Slide 31: Other ways to speed up games
Dynamic model complexity scaling
  This would be implemented in the engine, not shaders
Vertex Shader scaling
  This is a logical progression from the pixel shader approach and is essentially identical
Geometry Shader scaling
  Same as above
Notes: Dynamic scaling would use the game engine itself to determine model scaling, not the shaders

## Slide 32: Fragment Shader definition
void fshader(float4 l_position : POSITION,
float4 l_my_position: TEXCOORD0,
float2 l_texcoord0,
float3 l_lightvec,
float3 l_pointpos,
uniform float4 k_mousepos: C6,
uniform float4 mspos_light : C7,
sampler2D tex_0,
sampler2D tex_1,
out float4 o_color : COLOR)

## Slide 33: Fragment Shader implementation
// “point” is the location of the pixel itself on the screen
float2 point = float2(l_my_position[0]/l_my_position[3],l_my_position[1]/l_my_position[3]);
// “point2” is the location of the mouse on the screen
float2 point2 = float2(k_mousepos[0], k_mousepos[1]);
// in_area determines if the position of the pixel is within x distance of the mouse.
// k_mousepos[2] is actually a flag for enabling/disabling the effect.
bool in_area = (k_mousepos[2] > .9 && distance(point, point2) < .5) || k_mousepos[2] < .1;
// everything will be white if it’s in the center and white otherwise.
if (in_area)
o_color = float4(1,1,1,1);
else
o_color = float4(0,0,0,1);

## Slide 34: The End